| List of Bulletins for LOM in-line piston engines - from 2009-01-01 | 1 |
| --- | --- |
| No of Bulletin. | Valid for engines: | Valid from: | Concerns to: | Service | Information. |
| LOM-MB-01a/2009 | For M332, M337, M132, M137 all series engines. | Date of issue | The marking and use of the cut-down cylinder heads for M132, M332, M137, M337 engines of all models and versions. The heads are marked S1 or S2. | M | - |
| LOM-MB-02a/2009 | For M332, M337, M132, M137 all series engines. | July 1, 2009 | Possibilities of extending the calendar operating periods for the piston engines of model lines M332, M337, M137, M132 of all versions. The first revision of the original bulletin issued on 1st September, 1994. | M | - |
| LOM-MB-03a/2009 | M332, M337, M337A, M337AK, M137A. | August 14, 2009 | Additional check of airworthiness of the following engines M332, M337, M337A, M337AK, M137A. The operating period was extended for the following engines after February 2006 by the organisation W-MOTOR SERVICE, s.r.o. beyond their valid authorizations for this activity (after the cooperation agreement with LOM PRAHA s.p. was terminated in the system LOM ASSISTANCE). | M | - |
| LOM-IB-04b/2009 | For M332, M337, M132, M137 all series engines. | December 12, 2009 | Information for engine operation, and operation shortly after installation into the aircraft airframe. | - | M |
| LOM-MB-05a/2010 | For M332, M337, M132, M137 all series engines. | August 26, 2010 | Usage of engine oils with higher kinematic viscosity for summer operation of the M337, M332, M137, M132 engines of all versions, at which a drop in oil pressure occurs at idle running to the value of 100 kPa at oil temperature on engine oil inlet higher than 65°C and air temperature higher than 20°C. Application of experience from operation of the Z­142 CAF aircraft with the M337AK.1 engines for other engines. | M | - |

New numbering of bulletins introduction from 1st January, 2009 for in-line engines M337, M332, M137, M132 of all versions.

Last revision date: August 26, 2010.