| List of Bulletins for M337A engine - information | 1b |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337A/1 | M4-III/34 M6-III/39 M137A/5 M332/66 M337/70 | 28.12.1973 | Serviceability of the aviation gasoline (petrol), mark AVGAS 100L (GRADE 100/130), for air service of the M4-III, M6-III, M137A, M332, M337 and M337A aeroengines. |  | M |
| M337A/2 |  |  | Cancelled |  |  |
| M337A/3 | M6-III/42 M137A/9 M137AZ/9 M337/72 | 22.11.1976 | Reconstruction of the distributor arm and cam of the magneto LUN 2221.13 type 52-9276.57. |  | M |
| M337A/4 |  |  | Cancelled |  |  |
| M337A/5 | M137A/11 M137AZ/5 | 18.8.1977 | Service introduction of an improved modified fuel injection pump, type LUN 5150.01, serviceable for the aeroengines of types M137A, M137AZ,and M337A. |  | M |
| M337A/6b |  |  | Cancelled |  |  |
| M337A/7b |  |  | Cancelled |  |  |
| M337A/8b |  |  | Cancelled |  |  |
| M337A/9b |  |  | Cancelled |  |  |
| M337A/10b | M137A/15b M137AZ/8b M337/76b M337AK/5b | 15.12.1994 | The possibility of the prolognation of the operational time of M137A, M137AZ, M337, M337A and M337AK engines within the period till the first and subsequent overhaul. |  | M |
| M337A/11b | M137A/16b M137AZ/9b M337/78b M337AK/6b | 12.5.1995 | Increasing the time between overhauls (TBO) by 200 flight hours to the first overhaul and second overhaul for the following engines: M137A, M137AZ, M337, M337A and M337AK, which had their TBO prologned as per Information Bulletin No.:M137A/15b, M137AZ/8b, M337/76b, M337A/10b and M337AK/5b (from 800 flight hours to 1000 flight hours and respectively from 1000 to 1200 flight hours. |  | M |
| M337A/12b |  |  | Not issued. |  |  |

| List of Bulletins for M337A engine - information | 2b |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337A/13b | M332/68b M137A/18b M137AZ/11b M337/79b M337AK/8b | 29.1.1996 | Increasing the time between overhauls (TBO) on the basis of the type of aviation oil used in engines overhauled by LOM PRAHA after February 1 st 1996. |  | M |
| M337A/14b | M332/69b M137A/19b M137AZ/12b M337/80b M337AK/9b | 28.3.1996 | The possibility of utilization of mineral aircraft oils: Aero Shell Oil 100, Elf Aviation 100, Total Aero 100 and Mobil Aero Red Band, corresponding to the US specification MIL- L-6082E Grade 1100 as an equivalent for mineral aircraft oil MS-20 in flight operation of M332, M137A, M137AZ, M337, M337AK and M337A engines. |  | M |
| M337A/15b |  |  | Cancelled |  |  |
| M337A/16b | M332A/5b M332AK/4b M137A/21b M137AZ/14b M337AK/11b M337AK.1/4b M132A/2b M132AK/2b | 21.7.1997 | Introduction of modernised injection pump with automatic fuel mixture enrichement correction. |  | M |
| M337A/17b | M332/72b M332A/7b M332AK/6b M137A/22b M137AZ/15b M337/83b M337AK/12b M337AK.1/5b M132A/4b M132AK/5b | 6.10.1997 | Improvement of ignition magnetos sealing against oil leakage from engine crank case. |  | M |
| M337A/18b |  |  | Not issued. |  |  |
| M337A/19b | M137A/24b M137AZ/17b M337/87b M337AK/14b | 18.5.1998 | Possibilities of TBO prolonging from 1200hrs to 1400 hrs help of mineral oils using and from 1400hrs to 1600 hrs help of dispersed ash-free oils using. |  | M |

| List of Bulletins for M337A engine - information | 3b |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337A/20b/R1 | M137A/25b/R1 M137AZ/18b/R1 M337/88b/R1 M337AK/15b/R1 M332/77b/R1 | 3.12.2003 | TBO prolonging of M332 and M137/M337 engines-all versions, produced till 30.6.1991 (according to the type of used approved aircraft oil) in case of O/H will be executed in LOM PRAHA s.e. after 1.1.1999. |  | M |
| M337A/21b | M332/80b M332A/13b M332AK/12b M132A/10b M132AK/10b M137A/26b M137AZ/19b M337/91b M337AK/16b M337AK.1/11b M337B/3b M332B/3b | 15.11.1999 | Recommendation of ADX 776M additive for BL-78 fuel according to ČSN 65 6510. Incidences restriction of „valve-seat edge-folding“, which uniquelly occures on engines operated with BL-78 fuel. This fuel doesn´t include TEO. |  | M |
| M337A/22b/R1 | M332/81b/R1 M332A/14b/R1 M332AK/13bR1 M132A/11b/R1 M132AK/11bR1 M137A/27b/R1 M137AZ/20bR1 M337/92b/R1 M337A/22b/R1 M337AK/17bR1 | 17.10.2000 | Possibility of prescribed checking period increase from 50fl.hrs to 10010 fl.hrs or 12+1 months for engines M132, M332, M137, M337 manufactured in LOM Praha.sp or repaired and maintened in frame LOM ASSISTANCE system. |  | M |

| List of Bulletins for M337A engine - information | 4b |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337A/23b | M332/86b M332A/19b M332AK/18b M132A/15b M132AK/15b M137A/28b M137AZ/21b M337/97b M337AK/18b M337AK.1/16b | 15.11.2001 | Change of top limit cylinder head temperature for normal operating range to value 195o C ( 383 o F ). |  | M |
| M337A/24b | M332/87b M332A/20b M332AK/19b M332B/4b M132A/16b M132AK/16b M137A/29b M137AZ/22b M337/98b M337AK/19b M337AK.1/17b M337B/4b M337C/1b | 7.11.2001 Valid from 1.1.2002 | Possible use of BA91N, BA95N, BA98N vehicle gasolinesin accordance with CSN EN 228 in operation of M132, M332, M137 a M337 all version engines. |  | M |
| M337A/25b | M337AK/20b M337AK.1/19b | 16.6.2003 | Iddle motor oil pressure and motor rpm in operation of Z43 and Z142 all version planes powered by M337A, M337AK, M337AK.1 engines. |  | M |

| List of Bulletins for M337A engine - information | 5b |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M337A/26b | M332/88b M332A/21b M332AK/20b M332B/6b M332C/2b M132A/17b M132AK/17b M132C/2b M137A/30b M137AZ/23b M137C/2b M337/99b M337AK/21b M337AK.1/20b M337B/6b M337C/3b | 29.3.2005 | Possible use of minerál oil Exxon Mobil Aviation Oil EE100 for continuous flight operation of the M337, M332, M137, M132 engines in all versions |  | M |
| - | - | - | - | - | - |

Revision date : January 23, 2008