| List of Bulletins for M332 engine | 1 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| LM-120C/1 |  |  | Cancelled |  |  |
| M332/1 |  |  | Not issued. |  |  |
| M332/2 |  | 5.6.1959 | Completing the book „Decription, Service Instruction, Maintenance“ of the M332 engine part 5 „Attenance and Inspections of the engine“ by an instruction for cleaning and examination of the return-oil-filters. | M |  |
| M332/3 |  |  | Cancelled |  |  |
| M332/4 |  |  | Cancelled |  |  |
| M332/5 |  | 25.5.1959 | Depreservation of the Yc proming pum on the M332 engine. |  | M |
| M332/6 |  |  | Cancelled |  |  |
| M332/7 |  | 15.8.1959 | Comleting of technical specifications and remarks in the text of the M332 engine description, service instructions and maintenance manual. |  | M |
| M332/8 |  |  | Cancelled |  |  |
| M332/9 |  | 19.12.1959 | M332 engine starting. |  | M |
| M332/10 |  |  | Cancelled |  |  |
| M332/11 |  | 17.12.1959 | Maximum permissible instantanecus engine speed at 1,00 atm.abs. maximum boost pressure (nose dive). |  | M |
| M332/12 |  |  | Cancelled |  |  |
| M332/13 |  |  | Cancelled. |  |  |
| M332/14 |  |  | Cancelled |  |  |
| M332/15 |  |  | Cancelled |  |  |
| M332/16 |  |  | Cancelled |  |  |
| M332/17 |  |  | Cancelled |  |  |
| M332/18 |  |  | Cancelled |  |  |
| M332/19 |  |  | Cancelled |  |  |
| M332/20 |  |  | Cancelled |  |  |
| M332/21 |  |  | Cancelled |  |  |
| M332/22 |  |  | Cancelled |  |  |
| M332/23 |  |  | Cancelled |  |  |

| List of Bulletins for M332 engine | 2 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M332/24 |  |  | Cancelled |  |  |
| M332/25 |  |  | Cancelled. |  |  |
| M332/26 |  |  | Cancelled |  |  |
| M332/27 |  |  | Cancelled |  |  |
| M332/28 |  |  | Cancelled |  |  |
| M332/29 |  |  | Cancelled |  |  |
| M332/30 | M4-III/18 M6-III/13 M337/18 | 19.6.1961 | Removal and mounting circlips of piston pin at M4-III, M6-III, M332 and M337 engines. |  | M |
| M332/31 |  |  | Cancelled |  |  |
| M332/32 |  |  | Not issued. |  |  |
| M332/33 |  |  | Not issued. |  |  |
| M332/34 |  |  | Cancelled |  |  |
| M332/35 |  |  | Cancelled |  |  |
| M332/36 |  |  | Not issued. |  |  |
| M332/37 |  |  | Cancelled |  |  |
| M332/38 |  |  | Cancelled |  |  |
| M332/39 |  |  | Cancelled |  |  |
| M332/40 |  |  | Cancelled |  |  |
| M332/41 |  |  | Cancelled |  |  |
| M332/42 | M4-III/21 M6-III/18 M208B/23 M337/31 | 15.12.1962 | Bonding of the magnetos of the engine during its transportation and handling. |  | M |
| M332/43 |  |  | Cancelled |  |  |
| M332/44 |  |  | Cancelled |  |  |
| M332/45 |  |  | Cancelled |  |  |
| M332/46 |  |  | Cancelled |  |  |
| M332/47 | M337/36 | 23.2.1963 | Operation of M332 and M337 engines with increased rated power under exceptional climatic and operational conditions. |  | M |

| List of Bulletins for M332 engine | 3 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M332/48 |  |  | Cancelled |  |  |
| M332/49 | M4-III/24 M6-III/22 M337/39 V410 V506 | 27.3.1964 | Controll of the propeller hub tightening, appriopriatelly of oil distributor, on crankshaft. | M |  |
| M332/50 |  |  | Cancelled |  |  |
| M332/51 |  |  | Cancelled |  |  |
| M332/52 |  |  | Cancelled |  |  |
| M332/53 |  |  | Cancelled |  |  |
| M332/54 |  |  | Cancelled |  |  |
| M332/55 | M 4-III/29 M 6-III/27 M 337/50 | 16.9.1966 | Removal and installation of iston pin circlips at the M4-III, M6-III, M332 and M337 aeroengines. | M |  |
| M332/56 |  |  | Cancelled |  |  |
| M332/57 | M 4-III/30 M 6-III/28 M 337/52 | 23.9.1966 | Application of 100 octane fuel containing 0,079% T.E.O. |  | M |
| M332/58 | M337/53 | 14.7.1967 | Cylinder heads of M332 and M337 engines operated in Czech Republic, Slovak Republic and USSR: |  | M |
| M332/59 |  |  | Cancelled |  |  |
| M332/60 | M337/55 | 30.6.1968 | The use of PAL LUN 2141 regulator with Scintilla 600W 28 dynamo. |  | M |
| M332/61 |  |  | Cancelled |  |  |
| M332/62 |  |  | Cancelled |  |  |
| M332/63 | M337/61 | 6.12.1968 | Mounting of Sc 0377 couplinegs of distribution drive. | M |  |
| M332/64 |  |  | Cancelled |  |  |
| M332/65 |  |  | Cancelled |  |  |
| M332/66 | M4-III/34 M6-III/39 M137A/5 M337/70 M337A/1 | 28.12.1973 | The possibility of utilization of aircraft petrol AVGAS 100L (St.100/130) in the operation of M4-III, M6-III, M137A, M332, M337 and M337A engines. |  | M |

| List of Bulletins for M332 engine | 4 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M332/67a | M332A/1a M137A/14a M137AZ/9a M337/75a M337A/8a M337AK/5a | 7.9.1994 | How time (calendar monts) effect time between overhauls (TBO) for the following reciprocating engines M332, M332A, M332AK, M137, M137AZ, M337, M337A and M337AK. | M |  |
| M332/68b | M137A/18b M137A/11b M337/79b M337A/13b M337AK/8b | 20.1.1996 | Increasing the time between overhauls (TBO) on the basis of the type of aviation oil used in engines overhauled by LOM Prague, after February 1 st 1996. |  | M |
| M332/69b | M137A/19b M137AZ/12b M337/80b M337 A/14b M337AK/9b | 28.3.1996 | The possibility of utilization of mineral aircraft oils: Aero Shell Oil 100, Elf Aviation 100, Total Aero 100 and Mobil Aero Red Band, corresponding to the US specification MIL- L-6082E Grade 1100 as an equivalent for mineral aircraft oil MS-20 in flight operation of M332, M137A, M137AZ, M337, M337AK and M337A engines. |  | M |
| M332/70a | M332A/2a M332AK/1a M137A/15a M137AZ/10a M337/81a M337A/9a M337AK/6a M337AK.1/1a M332A/1a M132AK/1a | 6.6.1996 | Application of cylinder head Sc 2706 marked „Z“ together with special plain washers – cylinder head stud bolt nut Sc 1504R for all types and versions of engines stated above. | M |  |
| M332/71a |  |  | Cancelled |  |  |

| List of Bulletins for M332 engine | 5 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M332/72b | M332A/7b M332AK/6b M137A/22b M137AZ/15b M337/83b M337A/17b M337AK/12b M337AK.1/5b M132A/4b M132AK/5b | 6.10.1997 | Improvement of ignition magnetos sealing against oil leakage from engine crank case. |  | M |
| M332/73b |  |  | Not issued. |  |  |
| M332/74a |  | 6.10.1997 | M332 engine arrangement for hot conditions starting. | M |  |
| M332/75a | M332A/9a M332AK/8a M137A/17a M137AZ/12a M337/85a M337A/11a M337AK/8a M132A/6a M132AK/6a | 7.1.1998 | Precision of fuel mixture enrichement by engine starting, by engine operation in different flight levels and by landing. | M |  |
| M332/76a/R1 | M332A/10a/R1 M332AK/9a/R1 M332B/5a M332C/1a M137A/18a/R1 M137AZ/13a/R1 M137C/1a M337/86a/R1 M337A/12a/R1 M337AK/9a/R1 M337B/5a M337C/1a M132A/7a/R1 M132AK/7a/R1 M132C/1a | 3.12.2003 | Upgraded list of necessary documentation for checking, repairing, service and O/Hs. | M |  |

| List of Bulletins for M332 engine | 6 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M332/77b/R1 | M137A/25b/R1 M137AZ/18b/R1 M337/88b/R1 M337A/20b/R1 M337AK/15b/R1 | 3.12.2003 | TBO prolonging of M332 and M137/M337 engines-all versions, produced till 30.6.1991 (according to the type of used approved aircraft oil) in case of O/H will be executed in LOM PRAHA s.e. after 1.1.1999. |  | M |
| M332/78a | M332A/11a M332AK/10a M137A/19a M137AZ/14a M337/89a M337A/13a M337AK/10 M337AK.1/9a M132A/8a M132AK/8a M332B/1a M337B/1a | 18.12.1998 | Tightening moment for the tightening screws of oil pumps S/N : Sh 0059, Sh 0060, Sh 0060AK, Sc 0060 and Sh 0060A,B,C,D (for M337B, M332B engines). |  | M |
| M332/79a |  |  | Not issued. |  |  |
| M332/80b | M332A/13b M332AK/12b M132A/10b M132AK/10b M137A/26b M137AZ/19b M337/91b M337A/21b M337AK/16b M337AK.1/11b M337B/3b M332B/3b | 15.11.1999 | Recommendation of ADX 776M additive for BL-78 fuel according to ČSN 65 6510. Incidences restriction of „valve-seat edge-folding“, which uniquelly occures on engines operated with BL-78 fuel. This fuel doesn´t include TEO. |  | M |

| List of Bulletins for M332 engine | 7 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M332/81b/R1 | M332A/14b/R1 M332AK/13b/R1 M132A/11b/R1 M132AK/11b/R1 M137A/27b/R1 M137AZ/20b/R1 M337/92b/R1 M337A/22b/R1 M337AK/17R1 | 17.10.2000 | Possibility of prescribed checking period increase from 50fl.hrs to 10010 fl.hrs or 12+1 months for engines M132, M332, M137, M337 manufactured in LOM Praha.sp or repaired and maintened in frame LOM ASSISTANCE system. |  | M |
| M332/82a | M332A/15a M332AK/14a M132A/12a M132AK/12a M137A/20a M137AZ/15a M337/93a M337A/14a M337AK/11a | 23.10.2000 | The time restriction for idling operation during engine test on the ground for aircraft engines M337, M332, M137, M132 of all series. | M |  |
| M332/83a |  | 10.5.2001 | The precision of marking of engine M 332 | M |  |
| M332/84a |  |  | Cancelled |  |  |
| M332/85a | M332A/18a M332AK/17a M132A/14a M132AK/14a M137A/23a M137AZ/18a M337/96a M337A/17a M337AK/14a M337AK.1/1a | 22.10.2001 Valid from 1.1.2002 | Supplementary verification of airworthiness and issuance of authorized release certificate by an authorized person (form: JAA FORM ONE) for new or already used and repaired spare parts, assemblies, subassemblies and units (hereafter as: spare parts) for engines M337, M137, M332, M132 - all versions, for which no admissible documents confirming airworthiness have been issued, or which are doubtful. | M |  |

| List of Bulletins for M332 engine | 8 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| M332/86b | M332A/19b M332AK/18b M132A/15b M132AK/15b M137A/28b M137AZ/21b M337/97b M337A/23b M337AK/18b M337AK.1/1b | 15.11.2001 | Change of top limit cylinder head temperature for normal operating range to value 195o C ( 383 o F ). |  | M |
| M332/87b | M332A/20b M332AK/19b M332B/4b M132A/16b M132AK/16b M137A/29b M137AZ/22b M337/98b M337A/24b M337AK/19b M337AK.1/17b M337B/4b M337C/1b | 7.11.2001 Valid from 1.1.2002 | Possible use of BA91N, BA95N, BA98N vehicle gasolinesin accordance with CSN EN 228 in operation of M132, M332, M137 a M337 all version engines. |  | M |
| M332/88b | M332A/21b M332AK/20b M332B/6b M332C/2b M132A/17b M132AK/17b M132C/2b M137A/30b M137AZ/23b M137C/2b M337/99b M337A/26b M337AK/21b M337AK.1/20b M337B/6b M337C/3b | 29.3.2005 | Possible use of minerál oil Exxon Mobil Aviation Oil EE100 for continuous flight operation of the M337, M332, M137, M132 engines in all versions |  | M |

| List of Bulletins for M332 engine | 9 |
| --- | --- |
| No. | Identical with: | Valid from: | Concerns to: | Service | Information |
| - | - | - | - | - | - |

Revision date :   January 23, 2008